## Slide 1: Ethernet module

## Slide 2
Ethernet module initializations
Ethernet physical layer configurations
Ethernet negotiation with peer
Ethernet memory initializations
Ethernet MAC layer configurations
Ethernet protocol layer configurations
Event driven Ethernet transmission and reception
Platform initializations excluded
IP4v packet handler
Ethernet memory feeding
Ethernet BD feeding
Ethernet module enable
Ethernet ISR
Any bugs

## Slide 3
Protocol layer packet
Mac layer packet
Checksum
Ethernet packet format
Ip4v point to point protocol used. FCS polynomial as per ref. docs :
FCS(x) = x32+ x26+ x23+ x22+ x16+ x12+ x11+ x10+ x8+ x7+ x5+ x4+ x2+ x1+ 1

## Slide 4
Functional Reference
void ETH_init(int Clk, uint8_t * MACAddress):
Ethernet module initialization complete native module manipulation and initialization and then enabling of the ethernet module along with physical layer and memory initializatiion.
Args:
Clk : Data type int, core Clock of the microcontroller.
MACAddress : Pointer to the Mac address for the module
Complete module initialization
Functional colouring reference:
Return type
Function name
Arguments data type
Arguments name
Notes

## Slide 5
Functional Reference
uint16_t SD_ETH_write_IP_Packet(uint8_t* src, uint8_t* dest, uint8_t* IP_src, uint8_t* IP_dest, char * dataBuff):
Initializes the packet for IPv4 protocol fills IP packet structure that goes by the name SD_eth_test_t for further details take a look below.
Args:
src : Pointer to the Mac address for the source device.
dest : Pointer to the Mac address for the destination device.
IP_src: IPv4 address of source module.
IP_dest : IPv4 address of destination module.
dataBuff: Data buffer to by pushed to the packet.
Return:
Returns the length of the packet being transmitted.
Packet Handling

## Slide 6
Functional Reference
uint16_t ETH_write_ARP_Packet(uint8_t* src, uint8_t* dest, uint8_t* IP_src, uint8_t* IP_dest, uint16_t req_ans) :
Initializes the packet for IPv4 protocol fills IP packet structure that goes by the name SD_eth_test_t for further details take a look below.
Args:
src : Pointer to the Mac address for the source device.
dest : Pointer to the Mac address for the destination device.
IP_src: IPv4 address of source module.
IP_dest : IPv4 address of destination module.
req_ans : 1: request , 2 : reply.
Return:
Returns the length of the packet being transmitted.
Packet Handling

## Slide 7
Functional Reference
Crucial structures
SD_eth_test_t: Defination:
union __attribute__((__packed__))
{
struct __attribute__((__packed__))
{
eth_header_t HEADER;
IPv_4_ENET_PACKT_T IP4;
};
uint16_t rawBytes[((RAWLEN_16_t(300)) + 14)];
} SD_eth_test_t;
eth_header_t Header for ethernet
Packet Handling

## Slide 8
Functional Reference
Crucial structures
eth_header_t:
union __attribute__((__packed__))
{
struct __attribute__((__packed__))
{
  uint8_t dest[6]; //Pointer to the Mac address for the target device.
  uint8_t src[6]; // Pointer to the Mac address for the source device.
  uint16_t type; // protocol layer type
};
uint8_t rawBytes[ETH_HDR_LEN];
} eth_header_t;
Packet Handling

## Slide 9
Functional Reference
Crucial structures
IPv_4_ENET_PACKT_T
union __attribute__((__packed__))
{
struct __attribute__((__packed__))
{
uint8_t IP_HEAD_LEN_B:4;// IPv4 header length generally 5
uint8_t VER:4; //Version if IP protocol being used
uint8_t TOS; //Signal quality fields
uint16_t DATAGRAM_LENGTH_B; //length of datagram
uint16_t FRAGMENT_OFF; //The offset of the frame from beginning of the transmission
uint16_t FRAGMENT_ID; //The ID assigned to the fragment
uint8_t TTL; //Timeout for the frame to be valid
uint8_t PROTO; //IP protocol being used
uint16_t CHECK; // IPv4 checksum as per RFC_791
uint8_t SRC_IP[ETH_IP4ADDR_LEN]; // IPv4 address of source module
uint8_t DEST_IP[ETH_IP4ADDR_LEN]; // IPv4 address of destinationmodule
uint8_t DATA[300]; // Payload
};
uint16_t rawBytes[RAWLEN_16_t(300)];
} IPv_4_ENET_PACKT_T;
Packet Handling

## Slide 10
Functional Reference
Crucial structures
arp_packet_t
union __attribute__((__packed__))
{
struct arp_packet_s __attribute__((__packed__))
{
eth_header_t eth;
uint16_t htype; /* Network protocol type, Ethernet = 1 */
uint16_t ptype; /* Internetwork protocol, IPV4 = 0x0800 */
uint8_t hlen; /* Length of hardware address in octets = 6 */
uint8_t plen; /* Length of protocol address in octets = 4 */
uint16_t oper; /* Operation request=1, answer=2 */
uint8_t sha[ETH_ADDR_LEN]; /* sender hardware address */
uint8_t spa[ETH_IP4ADDR_LEN]; /* sender protocol address */
uint8_t tha[ETH_ADDR_LEN]; /* target hardware address */
uint8_t tpa[ETH_IP4ADDR_LEN]; /* target IP4 address */
};
uint16_t rawBytes[ETH_ARP_byte_LEN+ETH_HDR_LEN];
} arp_packet_t;
Packet Handling